### Overview
Network in Linux is configured via scripts. There are 2 locations for network:
- Udev Rules
- Sysconfig
The udev rules set the mapping between devices and users or any other system change which is needed. For example, during Oracle RAC installation, we have to set udev rules to change the owner of a specific iSCSI device to oracle user instead of root. During start up the udev deamon checks the rules and apply them. We can of course trigger the rules ourselves as we are going to see.
### Network interfaces
The default configuration location for network interfaces is at: /etc/sysconfig/network-scripts, in this folder, each interface has his own file with the necessary configuration which of course can be changed. In case a change is done, restart of the network interface should be done. This can be done by restarting:
- Network service
- Network Interface
Let's change our IP for example (bear in mind that the IP should be supported by the NIC)
We can see our network configuration as follows:
We can also see, the same settings in the following system configuration file:
If I change my IP from 129 → 130 and restart my network interface I should have different IP, right :) ?
This way we don't have to restart the whole network stack, there is however one problem with that procedure. What if we are connected to this IP and we change it, well you just lost your connection :) So if we do the same thing but we restart the whole service:
#### Modify DNS Search (Ubuntu)
To modify the DNS search location use the following commands:
Modify DNS Search domain
That command will modify the “Wired Connection 1” settings to search for flackboxA.lab domain.